## Slide 1: Firepower SDWAN
Bruno Fagioli
CCIE Security
10-Apr-24
Tectorial – From Zero to Hero
RECORD THE SESSION
Notes: 5min

## Slide 2: whoami
Cisco Partner Security TSA
20 anos na indústria de redes/cibersegurança
4 anos na Cisco
Líder SME em Access e Endpoint
Lider de segurança no Cisco CTF

## Slide 3
Introduction
VPN Overview
Tectorial Topologies
  Logical topology
  Physical topology
Tectorial Lab
  Interface configuration
  Routing and ECMP configuration
  DIA configuration
  SDWAN configuration
  SDWAN and WAN status

## Slide 4: Introduction

## Slide 5: Simplifying Branch Deployments
Secure Elastic Connectivity
Configure Route-based VPN VTI tunnels between branches (Spokes) to headquarters (Hubs)
IPv6 VTI with BGP
BGPv6 over VTI
EIGRP and OSPF over VTI
DVTI Support DHCP
High availability with near-Zero Network Down time / WAN Optimization
Dual ISP configuration
Active-Standby Backup VTI tunnel configuration with SLA Monitoring
Optimal Path Selection based on interface monitoring
Increased Usable Bandwidth
ECMP Support for load-balancing across multiple ISPs
ECMP Support for VTI
Application based load balancing using PBR
Direct Internet Access for Public Cloud and Guest Traffic
SaaS Application detection (First Packet using AVC)
DNS Snooping using trusted DNS servers
Policy Based Routing using Application as matching criteria
Local tunnel ID Support for Umbrella
Simplified Management
Data Interface Management
Auto Config Rollback
SASE: Umbrella Auto-tunnel deployment
DVTI Hub and Spoke topology simplification

## Slide 6: Direct Internet Access
DEPLOYMENT SCENARIO
For selective applications
For all SaaS applications
For specific users or networks or segments
BENEFITS
Faster access to cloud applications
Limit the need to back haul traffic to the data center
Accelerate your digital transformation
Corporate FTD
Corporate Network
Internet
Applications
Branch
FTD
Internal Clients
VTI Tunnels
DIA Traffic
Physical Connection
ECMP on VTI Interfaces
ISP1
ISP2
Routing application-based traffic directly out to the Internet rather than backhaul Device

## Slide 7: VPN Overview

## Slide 8: Underlay & Overlay
Underlay Network
Overlay Network
Notes: Before we go into various types of VPNs a quick recap on what is underlay and overlay. When we talk about VPNs, we often refer to an underlay and overlay network:
The underlay network is the network that is used as a transport for the VPN packets. It can be the Internet, MPLS, 4G or any other network.

## Slide 9: Underlay & Overlay
VPN
Underlay Network
Overlay Network
Notes: The overlay network is our private network that is built on top of the underlay.

## Slide 10: Introducing Front Door VRFs in 7.4
Support of VRFs for VTI comes in 7.4
Greatly reduces complexity by separating route tables of underlay and overlay
Increases security by creating defined VRF boundary
No competition between VPN learned routes and underly routes
DIA use cases are supported. Creation of NAT policy creates route-leaking that is required.
Outside
OUTSIDE
EIGRP
DHCP
Default
Branch
FTD
Hub
default
Front-Door VRF
global
INET

## Slide 11: What is SSE?
Notes: 5min

## Slide 12
Ivanti Study
believe the way they interact with technology directly impacts morale
64%
65%
believe they would be more productive if they had better technology
Employees are frustrated

## Slide 13: Market is moving to Security Service Edge
SSE is a cloud-based security service that provides safe access to Internet and private applications.
plan on adopting SSE in next 2 years
65%
SASE
SSE
Firewall as a Service (FWaaS)
Secure Web Gateway (SWG)
Cloud Access Security Broker (CASB)
Zero Trust Network Access (ZTNA)
SD-WAN
On-ramp into Public IaaS and Private Cloud
SD-WAN Analytics (including Internet Intelligence)
Secure SD-WAN Fabric
Performance-based Internet Routing
On-prem Unified Threat Management

## Slide 14: Firepower SDWAN Tectorial topologies
Notes: 15min

## Slide 15: Lab Logical Topology
Outside_gi3_40
198.60.62.100
OUTSIDE 198.18.133.81
Branch1
BGP
NGFW1
Hub
Outside_gi3_40
198.60.40.100
In10 198.19.10.1
Branch2
EIGRP
Outside_gi4_50
198.60.50.100
int_10: 198.19.11.0/24
int_20: 198.60.20.0/24
Outside_20
198.60.64.100
Branch3 OSPF
int_30: 198.60.30.0/24
Internet
198.19.20.0/24
198.19.30.0/24
198.19.40.0/24
Outside_gi4_30
198.60.162.100
Front-door
VRF ext
Notes: Branch1 – Outside_40 == Giga0/3 – 198.60.62.100
Branch1 – Outside_30 == Giga0/4 – 198.60.162.100

## Slide 16: Lab Logical Topology - detailed
Branch1
FTD
Hub
198.18.133.81/19
Branch2
198.19.11.0/24
198.60.20.0/24
vrf: branch2
CSR1: .61
198.19.10.1/24
Corporate2
198.19.20.0/24
vrf: corp2
CSR2: .62
Kali: .200
Branch3
198.60.30.0/24
vrf: branch3
CSR4: .64
vrf: corp3
CSR3: .63
Corporate3
198.19.30.0/24
vrf: corp4
CSR4: .64
Corporate4
198.19.40.0/24
Internet
Outside_gi3_40
198.60.62.100
Outside_gi3_40
198.60.40.100
Outside_gi4_30
198.60.162.100
Outside_gi4_50
198.60.50.100
Outside_20
198.60.64.100
Front-door
VRF ext
Notes: Branch2 – Outside_gi3_30 – address 40
Branch2 – Outside_gi4_40 – address 50

## Slide 17: SDWAN Topology
Branch1
FTD
Hub
198.18.133.81/19
Branch2
198.19.11.0/24
198.60.20.0/24
vrf: branch2
CSR1: .61
198.19.10.1/24
Corporate2
198.19.20.0/24
vrf: corp2
CSR2: .62
Kali: .200
Branch3
198.60.30.0/24
vrf: branch3
CSR4: .64
vrf: corp3
CSR3: .63
Corporate3
198.19.30.0/24
vrf: corp4
CSR4: .64
Corporate4
198.19.40.0/24
Internet
Outside_gi3_40
198.60.62.100
Outside_gi3_40
198.60.40.100
Outside_gi4_30
198.60.162.100
Outside_gi4_50
198.60.50.100
Outside_20
198.60.64.100
Via OSPF 198.19.40.0/24
Via EIGRP 198.19.30.0/24
Via EIGRP 198.60.20.0/24
Via OSPF 198.60.30.0/24
Front-door
VRF ext
Default BGP
BGP 198.19.11.0/24

## Slide 18: Lab Physical Topology
Branch1
FTD
Hub
198.60.40.0/24
198.18.128.0/19
Branch2
198.60.50.0/24
198.19.11.0/24
198.60.20.0/24
CSR
vrf: branch2
CSR1: .61
198.19.10.0/24
.133.60
.60
.1
.133.81
Corporate2
198.19.20.0/24
vrf: corp2
CSR2: .62
PC: .200
.100
.100
.1
.1
.100
Branch3
198.60.30.0/24
vrf: branch3
CSR4: .64
.100
vrf: corp3
CSR3: .63
Corporate3
198.19.30.0/24
vrf: corp4
CSR4: .64
Corporate4
198.19.40.0/24
CSR4
.1
Transit
198.19.12.0/24
.64
.60
198.60.64.0/24
.100
CSR2
.62
198.60.62.0/24
.1
.60
Transit
198.19.12.0/24
.100
198.60.162.0/24
.1
Front-door
VRF ext
Notes: Branch1 – Outside_40 == Giga0/3 – 198.60.62.100
Branch1 – Outside_30 == Giga0/4 – 198.60.162.100

## Slide 19: Tectorial files http://cs.co/9005nw2O5
Notes: 15min